## Slide 1
CDT-320
System Design (Manual-Compatible)
System Architecture & Design — 매뉴얼 3종 호환 (CDT-310 + CDT-300)
Submitted to : ASE
2026. 04. 29
"Taking this material out of the company without the authorization can be subject to restriction by the sales secret protection law."

## Slide 2
§1. 프로젝트 개요
Project Overview

## Slide 3
1.1 시스템 개요
3 / 15
CDT-310 매뉴얼 사양 + CDT-320 확장
프로젝트 정의
CDT-300 시리즈 듀얼 픽커 다이 본더 핸들러 — .NET 4.7.2 / WinForms 재구현
Vision PC + 3D 시뮬레이터 통합 (sim 모드 단독 검증 가능)
AJINEXTEK AXL 실보드 + Sim 자동 분기 (1 binary 양쪽 지원)
매뉴얼 3종 출처
ASEKorea_CDT-300_User_Manual_20181012.doc — CDT-300 운영 매뉴얼
2026.01.23_CDT310.docx — CDT-310 하드웨어/통신/IO 사양 (162KB)
2025.08.19_CDT310 Vision.docx — Vision 통신 사양 (40KB)
매뉴얼 호환 통신 채널 6종 (Stage 43 추가)
5100 — Wafer Vision Communicator
5101 — Inspection (Bottom) Vision Communicator
5103 — Bin Vision Communicator
5104 — Main Communicator (NEW)
5105 — TopSide Inspection Vision (NEW)
5106 — BottomSide Inspection Vision (NEW)
시리얼 포트 2종 (Stage 43 추가)
Port 4 — Wafer Barcode Communicator
Port 6 — Bin Barcode Communicator
"Taking this material out of the company without the authorization can be subject to restriction by the sales secret protection law."

## Slide 4
1.2 시스템 블록 다이어그램 (3 프로세스)
4 / 15
매뉴얼 사양 + Sim 통합
QMC.Vision (Cognex/OpenCV/Sim) ──────── 5100/5101/5103 +5104/5105/5106
QMC.CDT-320 (Handler) ──────── 6 Tabs / 5 권한 6 Unit + 25 Interlock Lot/Material/Job
CDT320Simulator (WPF 3D) ──────── TCP 7001 37 axes / IO Map
AJINEXTEK AXL Board 37 axes + DI/DO + Cylinders
Barcode Scanners Serial Port 4 / 6
라인 프로토콜 (Vision) + JSON HELLO (Sim) + P/Invoke AXL.dll (실보드)
"Taking this material out of the company without the authorization can be subject to restriction by the sales secret protection law."

## Slide 5
§2. 4-Layer 아키텍처
Layered Architecture

## Slide 6
2.1 Handler 4-Layer 구조
6 / 15
명확한 책임 분리
UI Layer — Form1 + 6 Tabs (Work/WorkInfo/History/Recipe/Settings/User) + 50+ Pages + 17 Dialogs
Controller — MachineController (Init/Start/Stop/CycleRun/Shutdown/EStop)
Equipment — CDT320_Machine + 6 Units + 25 Interlocks + Lot/Material/Job/SECS/Vision
HAL — BaseAxis / BaseDigitalIO / BaseCylinder + AjinFactory (Sim ↔ Ajin 자동 분기)
↓
↓
↓
UseAjin=true → AjinSystem.Open(IRQ) → P/Invoke AXL.dll / false → Sim* fallback
"Taking this material out of the company without the authorization can be subject to restriction by the sales secret protection law."

## Slide 7
§3. 6 Unit 통합 (Stage 28~32)
Equipment Layer Detail

## Slide 8
3.1 사이클 파이프라인 (좌→우 단방향)
8 / 15
모든 Unit + 사이클 통합 (Stage 28~32)
① Input Loader (Stage 26)
② Input Stage (Stage 28)
③ Transfer Picker (Stage 29)
④ Vision Inspection (Stage 31)
⑤ Output Stage (Stage 30)
⑥ Output Unloader (Stage 27)
단위층 — 각 Unit 의 메서드는 사이클 통합 전부터 정의됨 (LoadAndPrepare/Pickup/Receive 등)
ScanCassette MoveToTargetSlot MoveToExchange RetractFeeder
LoadAndPrepare VisionAlignAndSetupOrigin MultiScanAndPickup UnloadWafer
ArmX/ArmY 이동 PickerComponent Pickup/Place 4-Picker 동시
InspectBottom (4 picker) InspectSide (4면)
ReceiveDie (Good/Ng 분류) InspectBin (안착 검사)
ScanAllCassettes StoreFullWafer SupplyEmptyWafer ExchangeWafer
이벤트 — 매 8 다이마다 Output 적재, 매 24 다이마다 Collet Cleaning
"Taking this material out of the company without the authorization can be subject to restriction by the sales secret protection law."

## Slide 9
3.2 Unit 별 상세 (1)
9 / 15
InputLoader / InputStage / TransferPicker
InputLoaderUnit (Stage 26~28)
축: ElevatorZ (axis 0) / FeederY (axis 1)
실린더: FeederUpDownCyl / FeederClampCyl
센서: CassetteExist / Protrusion / WaferDetect / WaferClamped
메서드: ScanCassetteAsync / MoveToTargetSlotAsync / MoveToExchangePositionAsync / RetractFeederAsync
InputStageUnit (Stage 28)
축: StageY(2) / StageT(3) / ExpanderZ(4) / CameraX(5) / NeedleBlockX(6) / NeedleZ(7)
DO: NeedleVacuum
메서드: LoadAndPrepareWaferAsync (ExpanderZ Down + 바코드 + 맵 로드)
VisionAlignAndSetupOriginAsync (Theta 보정 + Origin 확정)
MultiScanAndPickupAsync / UnloadWaferAsync
TransferPickerUnit (Stage 29)
LeftArm (front): ArmX(9)/ArmY(10) + 4 Pickers (T11/Z12, T13/Z14, T15/Z16, T17/Z18)
RightArm (rear): ArmX(21)/ArmY(22) + 4 Pickers (T23/Z24 ~ T29/Z30)
각 Picker: PickupAsync (PickerZ Down + Vacuum) / PlaceAsync / MoveToFocusAsync
TpuArmUnit: InspectBottomVisionAsync / InspectSideVisionAsync / PlaceDiesAsync
"Taking this material out of the company without the authorization can be subject to restriction by the sales secret protection law."

## Slide 10
3.3 Unit 별 상세 (2)
10 / 15
Vision / OutputStage / OutputUnloader
VisionInspectionUnit (Stage 31)
TpuArmUnit 위임 (4 picker bottom 비전 + 4면 side 비전)
VisionHub.Inspection 미연결 시 sim fallback (skip)
Bottom Picker1 OffsetX/Y → ReceiveDieRequest.VisionOffsetX/Y
Side Picker1 IsAllOk → inspPass 반영
OutputStageUnit (Stage 30)
GoodStage (StageY/StageZ) + NgStage (StageY/StageZ)
BinCameraX (axis 34) — 안착 검사
메서드: ReceiveDieAsync (충돌 회피 + Z up + Y 이동)
InspectBinPositionAsync (TPU 완료 대기 + 비전 검사)
RequestWaferChangeAsync (Unloader 위임)
PerformColletCleaningAsync (NgStage 더미 영역)
OutputUnloaderUnit (Stage 27)
축: ElevatorZ (axis 36) / FeederY (axis 35)
3 카세트: NG / Good1 / Good2 (각 25 슬롯)
메서드: ScanAllCassettesAsync (75 슬롯 스캔)
StoreFullWaferAsync (target, slotIndex)
SupplyEmptyWaferAsync / ExchangeWaferSequenceAsync
"Taking this material out of the company without the authorization can be subject to restriction by the sales secret protection law."

## Slide 11
§4. 통신 + 인터락
Communications & Safety

## Slide 12
4.1 6 Vision 채널 + 시리얼 (매뉴얼 호환)
12 / 15
Stage 43 추가 채널
5100 Wafer Vision (matching/align)
5101 Inspection (Bottom)
5103 Bin Vision (안착)
5104 Main Communicator (NEW)
5105 Top Side Inspection (NEW)
5106 Bottom Side Inspection (NEW)
Serial Port 4 — Wafer Barcode
Serial Port 6 — Bin Barcode
SECS/HSMS Port 5000 (S6F11/S5F1)
모든 채널은 미연결 시 sim fallback — 단독 sim 검증 가능
"Taking this material out of the company without the authorization can be subject to restriction by the sales secret protection law."

## Slide 13
4.2 25 Interlock 등록
13 / 15
Stage 3 + 8 + 23 + 25
5 Standard (Stage 3 — ExtendedInterlocks.cs)
EjectVsLoaderInterlock / LoaderVsStageInterlock / UnloaderVsStageInterlock
EjectPickerVsBinInterlock / BinGuideVsBinFeederInterlock
5 Extended (Stage 8 — ExtendedInterlocks2.cs)
LifterVsExpanderInterlock / BarcodeVsLoaderInterlock
SubPortVsPickerInterlock / ColletCleanerVsPickerInterlock / EmgStopVsAllInterlock
5 ExtendedInterlocks3 (Stage 25)
DoorVsAllInterlock / WaferVisionZVsStageLifterInterlock
VacuumVsPickerInterlock / BinLidVsBinVisionInterlock / ServoOffInterlock
10 추가 (Stage 23 — 누적 25)
InterlockRegistry.VerifyMove(axisName, position, out reason)
차단 시 AlarmManager.Raise + false 반환 + 로그
Feeder 측 인터락
MoveElevatorWithProtrusionGuardAsync — 10ms ProtrusionSensor 폴링 + 즉시 EStop
"Taking this material out of the company without the authorization can be subject to restriction by the sales secret protection law."

## Slide 14
§5. 결론
Conclusion

## Slide 15
5.1 설계 완성도
15 / 15
매뉴얼 사양 + 32 Stage 확장
매뉴얼 호환
CDT-310 통신 6채널 (5100-5106) — Stage 43 추가
Wafer/Bin Barcode 시리얼 — Stage 43 추가
37 axis + 80+ DI/DO — Simulator IoMap 호환
4-Layer 아키텍처
UI / Controller / Equipment / HAL — 각 layer 독립
AjinFactory.Ready 검사 — 안전 fallback
6 Unit 사이클 통합 (Stage 27~32)
InputLoader → InputStage → TPU → Vision → OutputStage → OutputUnloader
모든 Unit 의 사이클 호출 경로 활성 + 종단 검증
검증
verify_all 117/118 PASS
auto-cycle 50 다이 — Yield 92% / ALARM 0
Lot JSON 자동 저장 16+ 개
"Taking this material out of the company without the authorization can be subject to restriction by the sales secret protection law."